## Slide 1: Chapter 1: Computer Network & Internet Computer Networking: A Top-Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley

## Slide 2: Outline
1.1 What is the Internet?
1.2 Network edge
  end systems, access networks, links
1.3 Network core
  network structure
1.4 Delay, loss and throughput
1.5 Protocol layers, service models (self-studying)
1.6 Networks under attack: security (self-studying)
1.7 History (self-studying)
Our goal: get “feel” some basic terminology and concepts.

## Slide 3: What’s the Internet?
millions of connected computing devices:
  hosts = end systems = end devices
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 3

## Slide 4: Growth of Internet Hosts

## Slide 5: Internet appliances

## Slide 6
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
mobile network
global ISP
regional ISP
home
network
institutional
network
What’s the Internet

## Slide 7: What’s the Internet: a service view
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 8: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 9
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 10: Outline
1.1 What is the Internet?
1.2 Network edge
  end systems, access networks, links
1.3 Network core
  network structure
1.4 Delay, loss and throughput
1.5 Protocol layers, service models
1.6 Networks under attack: security
1.7 History

## Slide 11: A closer look at network structure
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 12: Access networks and physical media
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent

## Slide 13: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 14: Ethernet Internet access
Typically used in companies, universities, etc…
10 Mbps, 100Mbps, 1Gbps, 10Gbps Ethernet
Today, end systems typically connect into Ethernet switch

## Slide 15: Home networks
Typical home network components:
  DSL or cable modem
  router/firewall/NAT
  Ethernet
  wireless access point

## Slide 16: Digital Subscriber Line (DSL)
uses existing telephone infrastructure
up to 1 Mbps upstream
up to 8 Mbps downstream
dedicated physical line to telephone central office

## Slide 17: Cable Network Architecture: Overview

## Slide 18: Residential access: cable modems

## Slide 19: Residential access: cable modems
uses cable TV infrastructure, rather than telephone infrastructure
HFC: hybrid fiber coax
  symmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable, fiber attaches homes to ISP router
  homes share access to router
  unlike DSL, which has dedicated access

## Slide 20: Outline
1.1 What is the Internet?
1.2 Network edge
  end systems, access networks, links
1.3 Network core
  network structure
1.4 Delay, loss and throughput
1.5 Protocol layers, service models
1.6 Networks under attack: security
1.7 History

## Slide 21: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 22: Network Core: Circuit Switching
end-end resources reserved for “call”
  link bandwidth, switch capacity
  dedicated resources: no sharing
  circuit-like (guaranteed) performance
  call setup required

## Slide 23: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
  pieces allocated to calls
  resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 24: Network Core: Packet Switching
Each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
Resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  node receives complete packet before forwarding

## Slide 25: Packet-switching: store-and-forward

## Slide 26: Internet structure: network of networks

## Slide 27: Tier-1 ISP: e.g., Sprint

## Slide 28: Internet structure: network of networks
“tier-2” ISPs: smaller (often regional) ISPs
connect to one or more tier-1 (provider) ISPs
  each tier-1 has many tier-2 customer nets
  tier 2 pays tier 1 provider
tier-2 nets sometimes peer directly with each other (bypassing tier 1) , or at IXP

## Slide 29: Internet structure: network of networks
“Tier-3” ISPs, local ISPs
customer of tier 1 or tier 2 network
  last hop (“access”) network (closest to end systems)

## Slide 30: Internet structure: network of networks
a packet passes through many networks from source host to destination host

## Slide 31: Outline
1.1 What is the Internet?
1.2 Network edge
  end systems, access networks, links
1.3 Network core
  network structure
1.4 Delay, loss and throughput
1.5 Protocol layers, service models
1.6 Networks under attack: security
1.7 History

## Slide 32: How do loss and delay occur?
packets queue in router buffers
  packet arrival rate to link exceeds output link capacity
  packets queue, wait for turn

## Slide 33: Four sources of packet delay

## Slide 34: Four sources of packet delay

## Slide 35: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.

## Slide 36: “Real” Internet delays and routes

## Slide 37: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 38: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time

## Slide 39: Throughput (more)

## Slide 40: Throughput: Internet scenario
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 41: Protocol “Layers”
Networks are complex, with many “pieces”:
hosts
routers
links of various media
applications
protocols
hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 42: Organization of air travel

## Slide 43: Layering of airline functionality
Layers: each layer implements a service
via its own internal-layer actions
relying on services provided by layer below

## Slide 44: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 45: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”

## Slide 46: (F&M) Figure 1.13: Communication through an internet

## Slide 47: (F&M) Figure 1.14: Logical connections between layers in TCP/IP

## Slide 48: Encapsulation

## Slide 49: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?

## Slide 50: Who runs Internet?
IP address & Internet Naming administered by Network Information Centre (NIC)
  Refer to: www.sgnic.net.sg; www.apnic.org
The Internet Society (ISOC) - Provides leadership in Internet related standards, education, and policy around the world.
The Internet Architecture Board (IAB) -Authority to issue and update technical standards regarding Internet protocols.
Internet Engineering Task Force (IETF) - Protocol engineering, development and standardization arm of the IAB.
  Internet standards are published as RFCs (Request For Comments)
  Refer to: www.ietf.org; for RFCs: http://www.ietf.org/rfc.html

## Slide 51: Internet Standards
Internet Standards are developed by IETF (Internet Engineering Task Force) www.ietf.org
IETF Standards documents are called RFCs (Request For Comments) http://www.ietf.org/rfc.html
They define protocols such as TCP, IP, HTTP, SMTP
There are nearly 7000 RFCs (July 2013)
LAN/MAN Standards – are defined by IEEE 802 LAN/MAN Standards Committee. (Ethernet, WiFi…) http://www.ieee.org/portal/site

## Slide 52: Outline
1.1 What is the Internet?
1.2 Network edge
  end systems, access networks, links
1.3 Network core
  network structure
1.4 Delay, loss and throughput
1.5 Protocol layers, service models
1.6 Networks under attack: security
1.7 History