## Slide 1
Chapter 3: Transport Layer
Computer Networking: A Top-Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley

## Slide 2: Chapter 3: Transport Layer
Our goals:
understand principles behind transport layer services:
  multiplexing/demultipl exing
  reliable data transfer
  flow control
  congestion control
learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 3: Chapter 3 outline
  Transport-layer services
  Multiplexing and demultiplexing
  Connectionless transport: UDP
  Principles of reliable
data transfer
  Connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management

## Slide 4: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in
end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 5: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services

## Slide 6: Internet transport-layer protocols
reliable, in-order delivery (TCP)
congestion control
flow control
connection setup
unreliable, unordered delivery: UDP
no-frills extension of
“best-effort” IP
services not available:
delay guarantees
bandwidth guarantees
application
transport network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
ne
twork
data link
physical
network
data link
physical
network
data link
physical
application
transport network
data link
physical
Notes: - Đảm bảo độ trễ
đảm bảo băng thông

## Slide 7: Chapter 3 outline
  Transport-layer services
  Multiplexing and demultiplexing
  Connectionless transport: UDP
  Principles of reliable
data transfer
  Connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management
  Principles of congestion control
  TCP congestion control

## Slide 8: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 9: How demultiplexing works
host receives IP
datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
32 bits
TCP/UDP segment format
source port # | dest port #
other header fields | 
application data (message) | 

## Slide 10: Connectionless demultiplexing
recall: created socket has host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 11: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 12: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 13: Connection-oriented demux (cont.)
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 14: Connection-oriented demux (cont.)
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 15: Chapter 3 outline
  Transport-layer services
  Multiplexing and demultiplexing
  Connectionless transport: UDP
  Principles of reliable
data transfer
  Connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management

## Slide 16: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP
segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 17: UDP: more
often used for streaming multimedia
apps
loss tolerant
rate sensitive
other UDP uses
DNS
SNMP
reliable transfer over UDP: add reliability at application layer
application-specific error recovery!
32 bits
UDP segment format
Length, in bytes of UDP
segment, including header
source port # | dest port #
length | checksum
Application data (message) | 

## Slide 18: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
NO - error detected
YES - no error detected. But maybe errors nonetheless? More later
….
Goal: detect “errors” (e.g., flipped bits) in transmitted
segment

## Slide 19: Internet Checksum Example
example: add three words 16-bit
1 0110011001100110
1 0101010101010101
0000111100001111
1100101011001010
0011010100110101
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result

## Slide 20: Chapter 3 outline
  Transport-layer services
  Multiplexing and demultiplexing
  Connectionless transport: UDP
  Principles of reliable
data transfer
  Connection-oriented transport: TCP
    segment structure
    reliable data transfer
    flow control
    connection management

## Slide 21: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 22: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 23: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 24: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 25: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
event causing state transition
actions taken on state transition
state 1
state 2
state: when in this “state” next state uniquely determined
by next event
event
actions

## Slide 26: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
rdt_rcv(packet)
extract (packet,data) deliver_data(data)
Wait for call from below
sender
receiver

## Slide 27: Rdt2.0: channel with bit errors
acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
How do humans recover from “errors”
during conversation?

## Slide 28: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection (checksum)
  receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 29: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
extract(rcvpkt,data) deliver_data(data) udt_send(ACK)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below

sender
receiver
rdt_send(data)

## Slide 30: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 31: rdt2.0: error scenario
3-30
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 32: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 33: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
Wait for ACK or NAK 0
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isNAK(rcvpkt) ) udt_send(sndpkt)
rdt_send(data)
sndpkt = make_pkt(1, data, checksum) udt_send(sndpkt)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for call 1 from above
Wait for ACK or NAK 1



## Slide 34: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for 0 from below
sndpkt = make_pkt(NAK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
Wait for 1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data) deliver_data(data)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum) udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum) udt_send(sndpkt)

## Slide 35: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will
suffice.
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 36: Recap
Rdt Version | Scenario | Features Added
1.0 | No error | Nothing
2.0 | Data Bit Error | Checksum, ACK/NAK
2.1 | Data Bit Error ACK/NAK Bit Error | Checksum, ACK/NAK, Sequence Number
3.0 | What else? | 

## Slide 37: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be
duplicate, but use of seq.
#’s already handles this
  receiver must specify seq
# of pkt being ACKed
requires countdown timer

## Slide 38: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum) udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isACK(rcvpkt,1) )
Wait for call 1 from above
sndpkt = make_pkt(1, data, checksum) udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt) && ( corrupt(rcvpkt) || isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt) start_timer
timeout
udt_send(sndpkt) start_timer
timeout
rdt_rcv(rcvpkt)
Wait for call 0from above
Wait for ACK1
rdt_rcv(rcvpkt)





## Slide 39: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 40: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 41: Recap
3-40
Rdt Version | Scenario | Features Added
1.0 | No error | Nothing
2.0 | Data Bit Error | Checksum, ACK/NAK
2.1 | Data Bit Error ACK/NAK Bit Error | Checksum, ACK/NAK, Sequence Number
3.0 | Data Bit Error ACK/NAK Bit Error Packet Loss | Checksum, ACK/NAK, Sequence Number, Timeout

## Slide 42: Performance of rdt3.0
rdt3.0 works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
U sender: utilization – fraction of time sender busy sending
U
sender=
.008
30.008
=
0.00027
L / R RTT + L / R
=
if RTT=30 msec, 1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources!
d  L  8000bits  8microseconds
R 109 bps
trans

## Slide 43: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0 last packet bit transmitted, t = L / R
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next packet, t = RTT + L / R
U
sender=
.008
30.008
=
0.00027
L / R RTT + L / R
=
Why send only one packet?
Can we send more?

## Slide 44: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to- be-acknowledged pkts
range of sequence numbers must be increased
buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N,
selective repeat

## Slide 45: Pipelining: increased utilization
sender receiver
first packet bit transmitted, t = 0 last bit transmitted, t = L / R
RTT
first packet bit arrives
last packet bit arrives, send ACK
last bit of 2nd packet arrives, send ACK last bit of 3rd packet arrives, send ACK
U
ACK arrives, send next packet, t = RTT + L / R
Increase utilization by a factor of 3!
sender=
.024
30.008
=
0.0008
3 * L / R RTT + L / R
=
How many packets should be in the pipeline?

## Slide 46: Bandwidth-Delay Product (BDP)
A logical link has a bandwidth of B bits/s and the round trip time is D sec.
Bandwidth-Delay Product or BDP is computed as B*D
Example:
  Two computers are connected over a WAN and can transfer data at 2Mbps with 100ms round trip time
 BDP = 2 * 0.1 = 0.2 Mb
  A satellite link has a bandwidth of 10Mbps and RTT of 1s
 BDP = 10 * 1 = 2 Mb
  Two computers from two universities in different continents are connected by a 500Mps link and has RTT of 200ms
• BDP = 500 * 0.2 = 100 Mb

## Slide 47: BDP Computation (cont’d)
How do you interpret BDP?
Why is BDP interesting?
BDP estimates on the amount of data that the
communicate pipe can “store”
  If the amount of unack data (window size) allowed is less than the BDP, sender will be idle at times, leading to lower efficiency

## Slide 48: Pipelined Protocols
Go-back-N: big picture:
sender can have up to N unacked packets in pipeline
rcvr only sends
cumulative acks
  doesn’t ack packet if
there’s a gap
sender has timer for oldest unacked packet
  if timer expires, retransmit all unack’ed packets
Selective Repeat: big pic
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only unack’ed packet

## Slide 49: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 50: Go-Back-N
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8

## Slide 51: Selective Repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACK’ed pkts